## Slide 1: INTRODUCTION TO ROS
ROBOTIC SYSTEMS(UE22EC342BC2) : AHP 2

## Slide 2: Launch Files
describe the configuration of the system and execute as described
what programs to run, where to run, what arguments to pass
monitoring, reporting and reacting to changes of state of processes
written in Python, XML or YAML
start and stop nodes, trigger and act on events
launch_ros package provides this framework.

## Slide 3: XML ROBOT DESCRIPTION FORMAT (URDF)
The Unified Robot Description Format (URDF) is an XML specification to describe a robot.
as general as possible, but obviously the specification cannot describe all robots
he main limitation at this point is that only tree structures can be represented, ruling out all parallel robots.
the specification assumes the robot consists of rigid links connected by joints; flexible elements are not supported.

## Slide 4: BASIC XML Structure (urdf)
the root element of the URDF format is a <robot> element.

## Slide 5: </link>
Inertial Properties (<inertial>)
  Defines the mass, center of mass, and moments of inertia of the link.
Visual Properties (<visual>)
  Defines how the link appears in simulation using shapes (<box>, <cylinder>, <sphere>, <mesh>).
  Can include material properties like color and texture.
Collision Properties (<collision>)
  Defines the simplified geometry used for physics-based collision checking.
  Often uses simpler shapes to reduce computation time.
Origin Transform (<origin>)
  Defines the position (xyz) and orientation (rpy) of the link relative to its parent.
URDF files are primarily used in ROS (Robot Operating System) for visualization (e.g., RViz), simulation (e.g., Gazebo), and motion planning

## Slide 6: </link>
Attributes
name (required) – Name of the link.
Elements
1. <inertial> (optional) – Defines mass and inertia properties.
<origin> (optional) – Position (xyz) and orientation (rpy) of the center of mass.
<mass> (required) – Mass value.
<inertia> (required) – Moments of inertia (ixx, iyy, izz, ixy, ixz, iyz).
2. <visual> (optional) – Defines appearance.
name (optional) – Name of the visual component.
<origin> (optional) – Offset (xyz, rpy) relative to the link frame.
<geometry> (required) – Defines shape:
  <box> – size (x, y, z).
  <cylinder> – radius, length.
  <sphere> – radius.
  <mesh> – filename, scale (optional).
<material> (optional) – Defines material properties:
  name (optional) – Material name.
  <color> (optional) – rgba (red, green, blue, alpha).
  <texture> (optional) – Texture filename.
3. <collision> (optional) – Defines collision geometry.
name (optional) – Name of the collision component.
<origin> (optional) – Offset (xyz, rpy) relative to the link frame.
<geometry> (required) – Same options as <visual>.
4. <collision_checking> (custom, optional)
Similar to <collision>, used for rough collision checking.

## Slide 7: </joint>
Attributes
name (required) – Specifies a unique name for the joint.
type (required) – Defines the type of joint, which can be:
  revolute – Rotates around an axis with defined limits.
  continuous – Rotates infinitely around an axis (no limits).
  prismatic – Slides along an axis with defined limits.
  fixed – Does not move (all DOFs locked).
  floating – Allows motion in all six DOFs.
  planar – Allows motion in a plane perpendicular to an axis.

## Slide 8: </joint>
Elements
1. <origin> (optional)
Defines the transformation from the parent link to the child link.
Attributes:
  xyz – Position offset (meters).
  rpy – Rotation (radians, roll-pitch-yaw order).
2. <parent> (required)
Specifies the parent link of the joint.
Attribute:
  link – Name of the parent link.
3. <child> (required)
Specifies the child link of the joint.
Attribute:
  link – Name of the child link.
4. <axis> (optional, default: (1,0,0))
Defines the axis of motion (rotation for revolute, translation for prismatic).
Attribute:
  xyz – A normalized vector (x, y, z).
5. <calibration> (optional)
Defines reference positions for joint calibration.
Attributes:
  rising – Trigger position for rising edge.
  falling – Trigger position for falling edge.
6. <dynamics> (optional)
Specifies physical properties for simulation.
Attributes:
  damping – Damping coefficient (N·s/m or N·m·s/rad).
  friction – Static friction force (N or N·m).
7. <limit> (required for revolute and prismatic joints)
Defines movement constraints.
Attributes:
  lower – Lower joint limit (radians or meters).
  upper – Upper joint limit (radians or meters).
  effort – Max force/torque applied.
  velocity – Max velocity (rad/s or m/s).
8. <mimic> (optional)
Makes a joint mimic another joint.
Attributes:
  joint – Name of the joint being mimicked.
  multiplier – Scaling factor.
  offset – Offset value (default: 0).
9. <safety_controller> (optional)
Sets safety limits.
Attributes:
  soft_lower_limit – Safety boundary (above lower limit).
  soft_upper_limit – Safety boundary (below upper limit).
  k_position – Relation between position and velocity limits.
  k_velocity – Relation between effort and velocity limits.

## Slide 9: HOW CAN YOU BECOME A ROS DEVELOPER?
MORE OF ROS 2 ON THE https://docs.ros.org/en/humble/index.html DOCUMENTATION, EXPLORE ALL THE TUTORIALS.